# Geology 140:  Investigations in Environmental Geology					Fall 2005

Assessment of Cullowhee Creek Restoration

Riparian, Channel, and Environmental Inventory (RCE)

Background

The Riparian, Channel, and Environmental Inventory (RCE) (Petersen 1992) was developed to quickly assess the physical and biological conditions of small streams in lowland, agricultural landscapes in temperate regions that have been physically modified.  The original RCE has been modified to better reflect local conditions.

More about this inventory....The inventory only characterizes a small stretch of a stream (about 100 m); conclusions about a watershed cannot be made from one site.  Remember that the quality of a stream water sample is a function of the entire upstream watershed--not just characteristics at the sampling site.  Furthermore, the inventory was developed to assess physical disruption of the channel and riparian zone.  Importantly, it does not assess the impact of point sources of pollution such as storm drainpipe discharges.

The inventory is used by estimating the values for fifteen characteristics over a selected length of the stream, usually about 100 m.  The highest score for each characteristic varies from 15-30 depending on the value of the characteristic to the overall index.  The highest total RCE score possible is 340; the lowest possible score is 1.  The fifteen characteristics included in the inventory all directly or indirectly relate to the biotic health of a stream.  For example, several characteristics of the physical structure of the stream are extremely important the quality of habit for aquatic life.  A channel undergoing a lot of erosion typically has an unstable bed and a low diversity of habitat types.

References

Petersen, Robert, 1992, The RCE: a riparian, channel, and environmental inventory for small streams in the agricultural landscape:  Freshwater Biology, volume 27, pages 295-306.

Norris, M., 1997, Adaptation of the riparian, channel and environmental inventory for use by high school students and for use on small streams of the French Creek Watershed (senior thesis)

Glossary

riparian zone:  area on the stream bank and next to stream bank

channel:  the physical structure that contains the stream; water only fills the entire channel when flooding.

stream:  the flowing water within the channel

riffle:  shallow, rapid areas, commonly on straight stream sections between bends

pool: deeper, usually calm areas of streams, commonly on the outside of river bends

detritus:  broken-down organic, particulate matter: ex. partially decomposed leaves, twigs; organic muck

INVENTORY:  Determine the condition of the stream CHANNEL and RIPARIAN ZONE between the two stakes you are assigned.  Estimate the average condition over that distance and for both sides of the channel.  Select ONE of the four scores for each characteristic.   Be sure to record the stream reach identification, that is, the stake number at the upstream and downstream ends of the reach assigned.

RCE Results:  A general guide to stream quality is listed below; however, it is best to use the RCE number for comparative purposes rather than for an absolute ranking.

Class	Score	Evaluation

I	273-340	Excellent

II	204-272	Very good

III	134-203	Good

IV	66-133	Fair

V	15-65	Poor

Riparian, Channel, and Environmental Inventory

modified from Petersen, 1992 and Norris, 1997 by FCEEP for FCEEP, 1997

| Observers: Date & Time of survey: |
| --- |
| Stream Reach ID: Upstream Stake = _______ Downstream Stake = _______ |
| Stream width in feet, estimate: | Stream depth in feet, estimate: |
| Stream flow condition: high, medium, or low | Days since last significant rain: 0 1 2 3 4-7 8+ |

I:  Land Use (115 points possible)

____	1. Land-use pattern beyond the immediate riparian zone

Undisturbed, consisting of forest and/or natural wetlands (30)

Mixture of trees and shrubs; few buildings & roads (20)

Athletic fields, or mixed grass lawn and small buildings (10)

Mainly parking lots, roads and buildings (1)

____	2. Width of riparian zone from stream edge to field

Trees, shrubs, or tall grasses in riparian zone >30 m wide (30)

Trees, shrubs, or tall grasses in riparian zone varying from 5 to 30 m (20)

Trees, shrubs, or tall grasses in riparian zone 1-5m (5)

Trees, shrubs, or tall grasses in riparian zone absent (1)

____	3. Completeness of riparian zone

Riparian zone intact without breaks in vegetation (30)

Breaks occurring at intervals of > 50 m (20)

Breaks frequent with some gullies and scars every 50 m (5)

Deeply scarred with gullies all along its length (1)

____	4. Vegetation of riparian zone within 10 m of the channel

>90% plant density of mature trees or shrubs, or native marsh plants (25)

Mixed young species along channel and mature trees behind (25)

Vegetation of mixed grasses and sparse young tree or shrub species (5)

Vegetation consisting mostly of grasses, few trees & shrubs; low plant density (1)

II. Physical Structure of Stream (165 points possible)

____	5. Debris dams

Channel with engineered structures, rocks and old logs firmly set in place (15)

Engineered structures, rocks and logs present but back filled with sediment (10)

Rocks or logs present, but loose, probably moving with floods (5)

Debris dams sparse or absent (1)

____	6. Channel width to depth ratio (ability to contain high flows)

width/depth <7; ample for present and annual peak flows (15)

width/depth 8-15; adequate, overbank flows rare (10)

width/depth 15-25; barely contains common  high flows (5)

width/depth >25 or stream is artificially channelized; overbank flow common (1)

____	7. Channel bars

Little or no channel width enlargement where coarse-grained bars present (15)

Some gravel bars, pore spaces between rocks well washed with little silt present (10)

Sediment bars of rocks, sand and silt common (5)

Channel divided into braids around sediment bars or stream is channelized (1)

____	8. Stream-bank stability

Banks stable, of rock and soil held firmly by grasses, shrubs, and tree roots (25)

Banks firm but loosely held by grass and shrubs (15)

Banks loose, held by a sparse layer of grass and shrubs (5)

Banks unstable, of loose soil or sand easily disturbed (1)

____	9. Bank undercutting

Little or none evident or restricted to areas with tree root support (20)

Bank undercutting only on curves and at channel constrictions (15)

Bank undercutting common, some banks falling in (5)

Severe bank undercutting along channel, banks falling in (1)

____	10. Stony substrate; feel and appearance

Stones clean, rounded without sharp edges; may have blackened color (25)

Stones without sharp edges and with slight gritty feel (15)

Some stones with sharp edges, obvious gritty feel (5)

Stones bright; sharp edges common (1)

____	11. Stream Bottom

Gravel and sand mixture; open pore spaces common between particles (25)

Loose stony bottom with some silt (15)

Mixture of silt, sand, and gravel; open pores sparse; bed firm in places (5)

Uniform bottom of sand and silt held loosely together, stony substrate absent (1)

____	12. Riffles and pools

Riffles distinct, occurring at intervals of 5-7 times the stream width (25)

Riffles and pools irregularly spaced (20)

Long pools separating short riffles (10)

Riffles and pools absent or stream channelized (1)

III. Biota (45 points possible)

____	13. Aquatic vegetation

When present consists of moss and patches of algae (15)

Algae dominant in pools, larger plants along edge (10)

Algal mats present, some larger plants, few mosses (5)

Algal mats cover bottom, larger plants dominate the channel (1)

____	14. Fish (Stand at the bank edge and observe quietly for a few minutes)

Fish present in most pools, multiple species (20)

Fish scarce and difficult to locate, multiple species (15)

Fish scarce, single species (5)

Fish absent (1)

____	15. Detritus

Mainly consisting of leaves and wood without sediment (25)

Leaves and wood scarce; fine organic debris without sediment (10)

No leaves or woody debris; coarse and fine organic matter with sediment (5)

Fine organic sediment - black in color and foul odor (anaerobic) (1)

| TOTALS | Stream Reach ID: stake ___ to stake ___ | Land Use subscore | Physical Structure subscore | Biota subscore | TOTAL RCE | Stream Class Ranking (I-V) |
| --- | --- | --- | --- | --- | --- | --- |