Riparian, Channel, and Environmental Inventory (RCE)

of Cullowhee Creek, WCU

Summarize your RCE results on the table below.  You must complete an RCE in each of the three stream reach types.   The natural area is downstream past Greek row—just keep walking along a path next to the stream until you turn right.  Soon after, you should find an opening where you can complete the RCE.   The restored reach RCE must be completed in an area that includes the a restoration structure (huge boulder shapes).  The disturbed reach RCE should be completed upstream of the restored portion of Cullowhee Creek in the area near the parking lots to the Ramsey Center and football field.

| Stream Reach ID: | Degree of stream reach alteration | Land Use subscore | Physical Structure subscore | Biota subscore | TOTAL RCE | Stream Class Ranking (I-V) |
| --- | --- | --- | --- | --- | --- | --- |
| N | natural |  |  |  |  |  |
| R | restored |  |  |  |  |  |
| D | disturbed |  |  |  |  |  |

# Geology 150 Lab				    Names __________________________

# WCU, Mark Lord, F05

Riparian, Channel, and Environmental Inventory (RCE)

Background

The Riparian, Channel, and Environmental Inventory (RCE) (Petersen 1992) was developed to quickly assess the physical and biological conditions of small streams in lowland, agricultural landscapes in temperate regions that have been physically modified.  The original RCE has been modified to better reflect local conditions.

More about this inventory....The inventory only characterizes a small stretch of a stream (about 100 m); conclusions about a watershed cannot be made from one site.  Remember that the quality of a stream water sample is a function of the entire upstream watershed--not just characteristics at the sampling site.  Furthermore, the inventory was developed to assess physical disruption of the channel and riparian zone.  Importantly, it does not assess the impact of point sources of pollution such as storm drainpipe discharges.

The inventory is used by estimating the values for sixteen characteristics over a selected length of the stream (suggested as 100 meters).  The highest score for each characteristic varies from 15-30 depending on the value of the characteristic to the overall index.  The highest total RCE score possible is 360; the lowest possible score is 16.  The sixteen characteristics included in the inventory all directly or indirectly relate to the biotic health of a stream.  For example, several characteristics of the physical structure of the stream are extremely important the quality of habit for aquatic life.  A channel undergoing a lot of erosion typically has an unstable bed and a low diversity of habitat types.

References

Petersen, Robert, 1992, The RCE: a riparian, channel, and environmental inventory for small streams in the agricultural landscape:  Freshwater Biology, volume 27, pages 295-306.

Norris, Marian,  1997, Adaption of the riparian, channel and environmental inventory for use by high school students and for use on small streams of the French Creek Watershed (senior thesis)

Glossary

riparian zone:  area on the stream bank and next to stream bank

channel:  the physical structure that contains the stream;  water only fills the entire channel when flooding.

stream:  the flowing water within the channel

riffle:  shallow, rapid areas, commonly on straight stream sections between bends

pool: deeper, usually calm areas of streams, commonly on the outside of river bends

detritus:  broken-down organic, particulate matter: ex. partially decomposed leaves, twigs; organic muck

darters: small, colorful, usually "dart" along stream bottoms; generally indicators of good water quality

sculpins:  spiny large-headed broad-mouthed usually scaleless fishes; generally indicators of good water quality

INVENTORY:  Determine the condition of the stream CHANNEL and RIPARIAN ZONE at which you are standing and up to 50 m upstream and downstream.  Estimate the average condition over that distance and select ONE of the four scores for each characteristic.

RCE Results:  A general guide to stream quality is listed below, however, it is best to use the RCE number for comparative purposes rather than for an absolute ranking.

Class	Score	Evaluation

I	273-340	Excellent

II	204-272	Very good

III	134-203	Good

IV	66-133	Fair

V	15-65	Poor

Riparian, Channel, and Environmental Inventory

modified from Petersen, 1992 and Norris, 1997  by FCEEP for FCEEP, 1997

| BASIC DATA |
| --- |
| Stream Reach ID: *plot location on map* | N-Natural (downstream of greek row) | R-Restored (by picnic area) | D-Disturbed (near Ramsey Center) |
| Observers |  |  |  |
| Stream width in m |  |  |  |
| Stream depth in m |  |  |  |
| Stream flow condition: high, medium, or low |  |  |  |
| Days since last significant rain: 0 1 2 3 4-7 8+ |  |  |  |
| Date & Time of survey |  |  |  |

I:  Land Use (115 points possible)                                                            Stream Reach ID          _N_  _R_  _D_

1.	Land-use pattern beyond the immediate riparian zone	___  ___  ___

Undisturbed, consisting of forest and/or natural wetlands (30)

Permanent pasture mixed with woodlots and wetlands; few buildings and roads (20)

Mixed row crops and pasture, or mixed grass lawn and homes (10)

Mainly row crops, or mostly streets, pavement, and buildings (1)

2.	Width of riparian zone from stream edge to field	___  ___  ___

Marshy or woody riparian zone >30 m wide (30)

Marshy or woody riparian zone varying from 5 to 30 m (20)

Marshy or woody riparian zone 1-5m (5)

Marshy or woody riparian zone absent (1)

3.	Completeness of riparian zone	___  ___  ___

Riparian zone intact without breaks in vegetation (30)

Breaks occurring at intervals of > 50 m (20)

Breaks frequent with some gullies and scars every 50 m (5)

Deeply scarred with gullies all along its length (1)

4.	Vegetation of riparian zone within 10 m of the channel	___  ___  ___

>90% plant density of mature trees or shrubs, or native marsh plants (25)

Mixed young species along channel and mature trees behind (25)

Vegetation of mixed grasses and sparse young tree or shrub species (5)

Vegetation consisting mostly of grasses, few trees  and shrubs; low plant density (1)

II. Physical Structure of Stream (165 points possible)

5.	Debris dams	___  ___  ___

Channel with rocks and old logs firmly set in place (15)

Rocks and logs present but back filled with sediment (10)

Debris dams loose, probably moving with floods (5)

Debris dams sparse or absent (1)

6.	Channel width to depth ratio (ability to contain high flows) 	___  ___  ___

width/depth <7; ample for present and annual peak flows (15)

width/depth 8-15; adequate, overbank flows rare (10)

width/depth 15-25; barely contains common  high flows (5)

width/depth >25 or stream is artificially channelized; overbank flow common (1)

7.	Channel bars	___  ___  ___

Little or no channel width enlargement  where coarse-grained bars present (15)

Some gravel bars,  pore spaces between rocks well washed with little silt present (10)

Sediment bars of rocks, sand and silt common (5)

Channel divided into braids  around sediment  bars or stream is channelized (1)

Stream Reach ID	 _N_  _R_  _D_

8.	Stream-bank stability	___  ___  ___

Banks stable, of rock and soil held firmly by grasses, shrubs, and tree roots (25)

Banks firm but loosely held by grass and shrubs (15)

Banks  loose, held by a sparse layer of grass and shrubs (5)

Banks unstable, of loose soil or sand easily disturbed (1)

9.	Bank undercutting	___  ___  ___

Little or none evident or restricted to areas with tree root support (20)

Band undercutting only on curves and at constrictions (15)

Band undercutting common, some banks falling in (5)

Severe bank undercutting along channel, banks falling in (1)

10.	Stony substrate; feel and appearance	___  ___  ___

Stones clean, rounded without sharp edges; may have blackened color (25)

Stones without sharp edges and with slight gritty feel (15)

Some stones with sharp edges, obvious gritty feel (5)

Stones bright; sharp edges common (1)

11.	Stream Bottom	___  ___  ___

Gravel and sand mixture; open pore spaces common between particles (25)

Loose stony bottom with some silt (15)

Mixture of silt, sand, and gravel; open pores sparse; bed firm in places (5)

Uniform bottom of sand and silt held loosely together, stony substrate absent (1)

12.	Riffles and pools	___  ___  ___

Riffles distinct, occurring at intervals of 5-7 times the stream width (25)

Riffles and pools irregularly spaced (20)

Long pools separating short riffles (10)

Riffles and pools absent or stream channelized (1)

III. Biota  (60 points possible)

13.	Aquatic vegetation	___  ___  ___

When present consists of moss and patches of algae (15)

Algae dominant in pools, larger plants along edge (10)

Algal mats present, some larger plants, few mosses (5)

Algal mats cover bottom, larger plants dominate the channel (1)

14.	Fish		___  ___  ___

Darters and sculpins present in most pools (20)

Darters and sculpins scarce and difficult to locate (15)

No darters or sculpin, other species in pools (5)

Fish absent or scarce (1)

15.	Detritus	___  ___  ___

Mainly consisting of leaves and wood without sediment (25)

Leaves and wood scarce; fine organic debris without sediment (10)

No leaves or woody debris; coarse and fine organic matter with sediment (5)

Fine organic sediment - black in color and foul odor (anaerobic) (1)

TOTALS:  	___  ___  ___

# Text boxes

Natural

Restored

Disturbed